## Slide 1
James Niffenegger
May 5, 2026
Variable Mass BEM Analysis Summary

## Slide 2
Meshes (.gdf files) made in Cubit of OC4 geometry with draft of 28 m
  Uniform surface meshes with sizes listed above
Capytaine used to calculate hydrostatics and hydrodynamics for drafts between 24 and 28 m (in intervals of 0.4 m)
  Capytaine also used to reduce draft of the meshes from 28 m
Mesh Sizes Considered
Mesh Size: 0.75
Mesh Size: 1
Mesh Size: 1.25

## Slide 3
All meshes cut at waterline with lids added to them (purple)
  All shifted 0.0001 above waterline to reduce error
Lid max face radius = 0.6
Capytaine Mesh Adjustments
Draft: 24 m
Draft: 26 m
Draft: 28 m

## Slide 4
Know the center of gravity (-13.46 m) for the 26 m draft model () so any change in draft is due to changes in water volume in the upper () and lower () ballasts
Change in displaced volume () determined using Capytaine:
  For simplicity: and mass is determined using water density (1,025 kg/m3)
Center of mass of these positive or negative volumes found using dimensions and the water levels in these cylinders according to the OC4’s specifications
  And the change in draft
Center of Gravity () Equation:
  is the mass of the 3 different bodies
  is the change in draft
Center of Gravity Calculations

## Slide 5
Change in Center of Gravity with Draft
Considering the change in ballast volume ( & ) insignificantly changes the center of gravity vs only accounting for the change in draft

## Slide 6: Added Mass at Infinity Comparison

## Slide 7
Added Mass at Infinity in Surge
Added mass (at infinity) in surge increases with increasing draft almost linearly
The added mass also decreases with decreasing mesh size

## Slide 8
Added mass (at infinity) in heave increases with draft
Added mass varies with mesh size
  Lowest added mass occurs with medium mesh size
  Highest added mass occurs with smallest mesh size
Added Mass at Infinity in Heave

## Slide 9
Added mass (at infinity) in heave increases with draft
Added mass nearly identical between mesh sizes of 0.75 and 1
Added Mass at Infinity in Pitch

## Slide 10: Mesh Comparison for Added Mass & Radiation Damping
Results for one draft size (24 m) for simplicity

## Slide 11
Added Mass in Surge
Results nearly identical between mesh sizes
Added mass decreases with decreasing mesh size

## Slide 12
Added Mass in Heave
Added mass varies inconsistently with mesh size

## Slide 13
Added Mass in Pitch
Results nearly identical between mesh sizes 0.75 and 1

## Slide 14
Radiation Damping in Surge
Results nearly identical between mesh sizes
Decrease with decreasing mesh size

## Slide 15
Radiation Damping in Heave
Results nearly identical between mesh sizes
Vary inconsistently with mesh size

## Slide 16
Radiation Damping in Pitch
Results nearly identical between mesh sizes
Vary inconsistently with mesh size

## Slide 17: Draft Comparison for Added Mass & Radiation Damping
Results for one mesh size (0.75) for simplicity

## Slide 18
Added Mass in Surge
Added mass consistently increases with increasing draft at all frequencies

## Slide 19
Added Mass in Heave
Added mass decreases with increasing draft at low frequencies (<1 rad/s)
Added mass increases with increasing draft above 1 rad/s

## Slide 20
Added Mass in Pitch
Added mass consistently increases with increasing draft at all frequencies

## Slide 21
Radiation Damping in Surge
Results nearly identical
Radiation damping varies inconsistently with increasing draft

## Slide 22
Radiation Damping in Heave
Radiation damping consistently increases with increasing draft at all frequencies

## Slide 23
Radiation Damping in Pitch
Radiation damping decreases with increasing draft at frequencies below 1 rad/s
Radiation damping increases with increasing draft at higher frequencies